## Slide 1: 6-DoF Semantics-Aware Condition- and Viewpoint-Invariant Visual SLAM
Principal Supervisor : Michael Milford
Associate Supervisor: Niko Sunderhauf
Confirmation of Candidature
Sourav Garg

## Slide 2: Contents
Introduction
Literature Review
Research Questions
Research Plan
Work Progress
Research Timeline

## Slide 3: Introduction
Social [1]
Domestic [2,3]
Industrial [4]
https://en.wikipedia.org/wiki/Pepper_(robot)#/media/File:SoftBank_pepper.JPG
Larry D. Moore CC BY-SA 3.0 -https://en.wikipedia.org/wiki/Domestic_robot#/media/File:Roomba_original.jpg
http://www.robotshop.com/en/robomow-rs622-robot-lawn-mower.html
https://www.businessinsider.com.au/rio-tinto-using-self-driving-trucks-to-transport-ore-2015-10?r=UK&IR=T

## Slide 4: SLAM
Simultaneous Localization and Mapping
  Landmarks in Environment
  Robot Pose
Approach
  Using Sensors like Laser Ranger
  Alternative:
  Camera
    Information-Rich
    Easy Access
    Inexpensive
Visual SLAM
ORB-SLAM2 - https://youtu.be/ufvPS5wJAx0

## Slide 5: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 6: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 7: Visual Place Recognition
Place Representation
  Local Features – SIFT, SURF, ORB etc.
    Bag of Words in FAB-MAP, ORB-SLAM etc.
  Global Representation – ConvNet, HoG etc.
    Direct Matching in LSD-SLAM, SeqSLAM etc.

## Slide 8: Challenging Environmental Conditions
Seasonal Variations in Nordland (Sunderhauf 2013)
SeqSLAM - Sunny Days vs Stormy Nights (Milford 2012)
Non-linear Intensity Deformation by Automatic Camera Settings (Alismail 2017)

## Slide 9: Place Recognition – Summary
Local Image Features
  Robust to viewpoint variations
Global Representations
  Robust to appearance variations
Deep-learned features
  Robust to both
Lack ability to estimate relative 3D pose for matches

## Slide 10: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 11: Visual Odometry
Matching consecutive images for Ego-motion estimation
Methods
  Feature Correspondence
  Direct Whole Image Matching
  Hybrid Methods
  Deep Learning Based
Challenges
  Abrupt Appearance variations
  Low light environment
  Rapid Camera Motion
  Motion Blur
VO Failure is catastrophic for Visual SLAM
(Alismail 2016)

## Slide 12: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 13: Representation Map
Types of Maps
  Topological, Metric or Topometric
3-D Reconstruction of Environment
  6-DoF Visual SLAM systems
  Sparse, Semi-Dense or Dense Reconstruction
Semantics in Maps
  Meaningful interaction with environment
Probabilistic Semi-Dense Mapping (Mur-Artal 2015)
Place Categorization and Semantic Mapping (Sunderhauf 2016)

## Slide 14: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map
Semantics?

## Slide 15: Semantics in Vision
Semantics within an Image
  Object Recognition
  Sparse or Dense Object Segmentation.
Place Semantics
  Place-centric vs Object-centric
  Place Categories and Attributes
Object Detection Using Faster R-CNN (Ren 2015)
(Zhou 2014)
Type of environment
outdoor
Semantic categories:
coast:0.35, ocean:0.30, boardwalk:0.07

## Slide 16: Semantics in Visual SLAM
Object-Oriented
    Matching Object 3-D Models
    Objects as Landmarks
  Mostly Indoor
Place-Oriented
    Semantic Mapping
Ideal Environmental Conditions
Multi-Object SLAM (Dharmasiri 2016)

## Slide 17: Research Gap
Visual Place Recognition
  Viewpoint- and Condition-Invariance
  With 3D Relative Pose Estimation
Visual Odometry
  Robustness to Dynamic Conditions
  Hybrid Approach
Representation Map
  Semantic Maps on top of Geometric Maps
Semantics for places
  Use Semantics to improve place recognition

## Slide 18: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 19: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 20: Characterizing System’s Response
Variations in Viewpoint and Environmental Conditions
  Visual SLAM
    Place Recognition
    Visual Odometry
  Performance Evaluation
    Using Real and Simulated Data
(Skinner 2016)
viewpoint- and condition-invariant

## Slide 21: Adapting to Challenging Conditions
Low Light, Rapid Movement, Variable Speed
  Hybrid Visual Odometry
    Using state-of-the-art VO with
    Coarse Ego-motion Estimation for
      Adapting System Parameters or
      Backing up during failure
  Improving Place Recognition Using Motion Cues
viewpoint- and condition-invariant

## Slide 22: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 23: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 24: Semantic Segmentation of Environment
Planned Approach
  Semantic Place Categorization
  Temporal Clustering of Semantic Labels
    Segment Environment
      Office Space - Cubicles, Canteen, Corridor, Restroom etc.
      Vehicle on Roads - Urban Canyon, Highway, Tunnel etc.
      House – Bedroom, Kitchen, Lawn, Stairs etc.
Place Categorization and Semantic Mapping (Sunderhauf 2016)
semantics-aware, condition-invariant

## Slide 25: Semantic Segmentation of Environment
Expected Outcome
  Seamless Transitions Within Environment
    Indoor/Outdoor, Naturally/Artificially Lit, Bland/Cluttered
    Benchmark place recognition performance against state-of-the-art methods
  Categorize and Recognize in a Reduced Search Space
    Coarse Semantic Localization
    Study Computational Gain and Performance Effects for very large databases
semantics-aware, condition-invariant

## Slide 26: Semantic Segmentation Within Image
Planned Approach
  Use state-of-the-art semantic segmentation
    Object-level or Pixel-level
  Learn semantically salient objects/regions for place recognition
Semantic Annotations (Mottaghi 2014)
semantics-aware, condition-invariant

## Slide 27: Semantic Segmentation Within Image
Expected Outcome
  Determine Condition-Dependent Objects/Regions
  Determine Dynamic Objects
  Evaluate Performance with Semantic Masking
  Performance Benchmark for place recognition with
    A large number of dynamic objects and
    Extreme condition variations
semantics-aware, condition-invariant

## Slide 28: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 29: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 30: Appearance-Robust 3-D Relative Pose
Planned Approach
  Condition-Invariant Image Representation
    Exploring Bit-Planes Descriptor (Alismail 2016)
  Direct Image Alignment in LK framework
    Descriptor Constancy vs Brightness Constancy
Expected Outcome
  3D Relative Pose Estimation for Condition-Invariant Place Recognition
  6-DoF Condition-Invariant Visual SLAM system
  Benchmark Performance against state-of-the-art
8-Channel Bit-Plane Descriptor can be used within a multi-channel LK framework using SSD cost measure (Alismail 2016)
6-DoF, condition-invariant

## Slide 31: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 32: An Integrated System
Planned Approach
  Semantic Mapping and System Integration
    Hybrid Visual Odometry
    Visual Place Recognition
      Semantic Awareness
    3-D Relative Pose for Loop Closures
Expected Outcome
  3-D Semantically-Interactive Map of Environment
  Semantic Navigation Goals
Object Oriented Semantic Mapping (Sunderhauf 2016)
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system

## Slide 33: Work Progress
Performance Evaluation using High-Fidelity Simulation
  Place Recognition – SeqSLAM
  Visual SLAM – ORB-SLAM
Adapting to Environment
  Transitions within Environment
  Improving Condition-Invariant Place Recognition
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 34: Work Progress
Performance Evaluation using High-Fidelity Simulation
  Place Recognition – SeqSLAM
  Visual SLAM – ORB-SLAM
Adapting to Environment
  Transitions within Environment
  Improving Condition-Invariant Place Recognition
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 35: Characterizing Visual SLAM
Performance Evaluation Using High-Fidelity Simulation
(Skinner 2016)
SeqSLAM – Place Recognition
ORB-SLAM – Visual SLAM
Viewpoint Varies
Time of Day
Notes: Varying time of day and viewpoint – data showing first image of different traversals
Top left is reference and rest are query datasets
Place Rec. performance , vSLAM is error
Takeaway is understanding sensitivity of systems using simulation data

## Slide 36
Performance Comparison
  Real vs Simulated
Real
Simulated
Later Camera Offset

## Slide 37
Accepted at IROS’16
  High-fidelity simulation for evaluating robotic vision performance
    Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M.

## Slide 38: Work Progress
Performance Evaluation using High-Fidelity Simulation
  Place Recognition – SeqSLAM
  Visual SLAM – ORB-SLAM
Adapting to Environment
  Transitions within Environment
  Improving Condition-Invariant Place Recognition
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 39: Adapting to Variations Within Environment
Semantic Place Categorization
Label
  0 - Outdoor
  2 - Indoor

## Slide 41
Parking Lot Data
  From Basement to Open Parking
Day Traverse
Night Traverse

## Slide 42
Accepted at IROS’17
  Improving Condition- and Environment-Invariant Place Recognition with Semantic Place Categorization
    Garg, S., Jacobson, A., Kumar, S. and Milford, M.

## Slide 43: Work Progress
Performance Evaluation using High-Fidelity Simulation
  Place Recognition – SeqSLAM
  Visual SLAM – ORB-SLAM
Adapting to Environment
  Transitions within Environment
  Improving Condition-Invariant Place Recognition
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 44: Ego-motion for Challenging Conditions
Self-Similarity Matrix

## Slide 45
Challenges
  Depends on Environment
  Is 1-D
Planned Usage
  Hybrid Visual Odometry System
    Backup for Challenging Environmental Conditions
    Adapting parameters for Rapid Motion

## Slide 46: Improving Place Recognition Using Motion Cues
Dynamic Frame Sampling
  Pick frames ‘n’ units apart
Vehicle Moving in Heavy Traffic Conditions
(Pepperell 2014)
Vanilla SeqSLAM
Proposed Method

## Slide 47: Target Publications
Ego-motion Estimation for Low-Light and Rapid Camera Motion
  ICRA’18
Semantic Segmentation of Environment
  IROS’18
Semantic Segmentation Within an Image
  ICRA’19
Appearance-Robust Relative 3-D Pose Estimation
  IROS’19
6-DoF Semantics-Aware Visual SLAM
  IJRR/TRO

## Slide 48: PhD Timeline

## Slide 49: References
Engel, Jakob, Thomas Schöps, and Daniel Cremers. "LSD-SLAM: Large-scale direct monocular SLAM." European Conference on Computer Vision. Springer International Publishing, 2014.
Sünderhauf, N., Neubert, P. and Protzel, P., 2013, May. Are we there yet? Challenging SeqSLAM on a 3000 km journey across all four seasons. In Proc. of Workshop on Long-Term Autonomy, IEEE International Conference on Robotics and Automation (ICRA) (p. 2013).
Alismail, H., Kaess, M., Browning, B. and Lucey, S., 2017. Direct Visual Odometry in Low Light Using Binary Descriptors. IEEE Robotics and Automation Letters, 2(2), pp.444-451.
Milford, M.J. and Wyeth, G.F., 2012, May. SeqSLAM: Visual route-based navigation for sunny summer days and stormy winter nights. In Robotics and Automation (ICRA), 2012 IEEE International Conference on (pp. 1643-1649). IEEE.
Cummins, M. and Newman, P., 2007, April. Probabilistic appearance based navigation and loop closing. In Robotics and automation, 2007 IEEE international conference on (pp. 2042-2048). IEEE.
Alismail, H., Browning, B. and Lucey, S., 2016, October. Robust tracking in low light and sudden illumination changes. In 3D Vision (3DV), 2016 Fourth International Conference on (pp. 389-398). IEEE.
Mur-Artal, R. and Tardós, J.D., 2015, July. Probabilistic Semi-Dense Mapping from Highly Accurate Feature-Based Monocular SLAM. In Robotics: Science and Systems.
Sünderhauf, N., Dayoub, F., McMahon, S., Talbot, B., Schulz, R., Corke, P., Wyeth, G., Upcroft, B. and Milford, M., 2016, May. Place categorization and semantic mapping on a mobile robot. In Robotics and Automation (ICRA), 2016 IEEE International Conference on (pp. 5729-5736). IEEE.

## Slide 50: References
Ren, S., He, K., Girshick, R. and Sun, J., 2015. Faster r-cnn: Towards real-time object detection with region proposal networks. In Advances in neural information processing systems (pp. 91-99).
Zhou, B., Lapedriza, A., Xiao, J., Torralba, A. and Oliva, A., 2014. Learning deep features for scene recognition using places database. In Advances in neural information processing systems (pp. 487-495).
Laffont, P.Y., Ren, Z., Tao, X., Qian, C. and Hays, J., 2014. Transient attributes for high-level understanding and editing of outdoor scenes. ACM Transactions on Graphics (TOG), 33(4), p.149.
Dharmasiri, T., Lui, V. and Drummond, T., 2016, October. MO-SLAM: Multi object SLAM with run-time object discovery through duplicates. In Intelligent Robots and Systems (IROS), 2016 IEEE/RSJ International Conference on (pp. 1214-1221). IEEE.
Jia, Y., Shelhamer, E., Donahue, J., Karayev, S., Long, J., Girshick, R., Guadarrama, S. and Darrell, T., 2014, November. Caffe: Convolutional architecture for fast feature embedding. In Proceedings of the 22nd ACM international conference on Multimedia (pp. 675-678). ACM.
Sünderhauf, N., Pham, T.T., Latif, Y., Milford, M. and Reid, I., 2016. Meaningful Maps $-$ Object-Oriented Semantic Mapping. arXiv preprint arXiv:1609.07849.
Alismail, H., Browning, B. and Lucey, S., 2016. Bit-planes: Dense subpixel alignment of binary descriptors. arXiv preprint arXiv:1602.00307.
Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M., 2016, October. High-fidelity simulation for evaluating robotic vision performance. In Intelligent Robots and Systems (IROS), 2016 IEEE/RSJ International Conference on (pp. 2737-2744). IEEE.
Mottaghi, R., Chen, X., Liu, X., Cho, N.G., Lee, S.W., Fidler, S., Urtasun, R. and Yuille, A., 2014. The role of context for object detection and semantic segmentation in the wild. In Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition (pp. 891-898).

## Slide 51: Thank You!

## Slide 52: Research Plan
Adapting Visual Odometry and Place Recognition
  Characterizing Response to Condition and Viewpoint Variations
  Coarse Ego-motion Estimation for Low Light and Rapid Movement
Semantics for Visual Place Recognition
  Semantic Segmentation Across Places
  Semantics Segmentation Within Places
6-DoF Semantics-Aware Visual SLAM
  Appearance-Robust 3-D Relative Pose
  An Integrated System

## Slide 54
(Skinner 2016)

## Slide 55: Some Challenges in Visual Odometry
Motion Blur
Low Light Environment
Illumination Variation
(Alismail 2016)

## Slide 56
Probabilistic Semi-Dense Mapping (Mur-Artal 2015)
Place Categorization and Semantic Mapping (Sunderhauf 2016)

## Slide 57
Object Detection Using Faster R-CNN (Ren 2015)
Multi-Object SLAM (Dharmasiri 2016)
Transient Attributes for Outdoor Scene Editing (Laffront 2014)
Scene Recognition Using Places Database (Zhou 2014)

## Slide 58: Research Questions
How can we characterize a visual SLAM system’s response to variations in environment and ego-motion, and make it more robust?
How can visual semantic information improve the robustness and generality of visual place recognition?
How can we develop a 6-DoF semantics-aware SLAM system that is robust to condition and viewpoint variations?

## Slide 59: Research Questions
How can we characterize a visual SLAM system’s response to variations in environment and ego-motion, and make it more robust?
How can visual semantic information improve the robustness and generality of visual place recognition?
How can we develop a 6-DoF semantics-aware SLAM system that is robust to condition and viewpoint variations?

## Slide 60: Research Questions
How can we characterize a visual SLAM system’s response to variations in environment and ego-motion, and make it more robust?
How can visual semantic information improve the robustness and generality of visual place recognition?
How can we develop a 6-DoF semantics-aware SLAM system that is robust to condition and viewpoint variations?

## Slide 61: Research Questions
How can we characterize a visual SLAM system’s response to variations in environment and ego-motion, and make it more robust?
How can visual semantic information improve the robustness and generality of visual place recognition?
How can we develop a 6-DoF semantics-aware SLAM system that is robust to condition and viewpoint variations?