## Slide 1: 6-DoF Semantics-Aware Condition- and Viewpoint-Invariant Visual SLAM
Principal Supervisor : Michael Milford
Associate Supervisor: Niko Sunderhauf
Confirmation of Candidature
Sourav Garg

## Slide 2: Contents
Introduction
Literature Review
Research Gap
Research Plan
Work Progress
Research Timeline
Notes: We will first go through the introduction of the research problem.
Then, explore the corresponding literature to figure out the research gap and propose a research plan.
Finally, we will go through the work progress to date, followed by a research timeline.

## Slide 3: Introduction
Social [1]
Domestic [2,3]
Industrial [4]
https://en.wikipedia.org/wiki/Pepper_(robot)#/media/File:SoftBank_pepper.JPG
Larry D. Moore CC BY-SA 3.0 -https://en.wikipedia.org/wiki/Domestic_robot#/media/File:Roomba_original.jpg
http://www.robotshop.com/en/robomow-rs622-robot-lawn-mower.html
https://www.businessinsider.com.au/rio-tinto-using-self-driving-trucks-to-transport-ore-2015-10?r=UK&IR=T

## Slide 4: SLAM
Simultaneous Localization and Mapping
  Realize Landmarks in Environment
  Localize in Map
Approach
  Using Sensors like Laser Ranger
  Alternative:
  Camera
    Information-Rich
    Easy Access
    Inexpensive
Visual SLAM
Hokuyo Scanning Laser Rangefinder [1]
[1] https://www.hokuyo-aut.jp/search/single.php?serial=167
Logitech C170 [2]
[2] https://www.logitech.com/en-au/product/webcam-c170
Motorola Moto G4 Play [3]
[3] https://www.motorola.com.au/products/moto-g-play
https://au.mathworks.com/help/physmod/sm/ref/6dofjoint.html
Turtlebot in Gazebo Simulator
http://babel.isa.uma.es/crumb/index.php/2016/03/10/how-to-simulate-turtlebot-in-rosgazebo/
Robot
Landmarks

## Slide 5: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 6: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 7: Visual Place Recognition
Place Representation
  Multiple Local Features
    SIFT (Lowe 2004), BRIEF (Calonder 2010), etc.
Method
  Bag of Words
    FAB-MAP (Cummins 2008)
  Feature Correspondence
    ORB-SLAM (Mur-Artal 2015)
BRIEF Keypoints (Calonder 2010)
Image - http://scikit-image.org/docs/dev/auto_examples/
Feature Correspondence
Recognizing a revisited place

## Slide 8: Visual Place Recognition
Place Representation
  Global Image Signature
    HoG (Dalal 2005), ConvNet (Sunderhauf 2015) etc.
Method
  Signature Matching
  Dense Image Matching
      LSD-SLAM (Engel 2014), SeqSLAM (Milford 2012) etc.
Image - http://scikit-image.org/docs/dev/auto_examples/
Histogram of Oriented Gradients - HoG (Dalal 2005)

## Slide 9
Seasonal Variations in Nordland (Sunderhauf 2013)
SeqSLAM - Sunny Days vs Stormy Nights (Milford 2012)
Condition-Invariance
  Extreme Changes in Appearance
    Seasons
    Time of Day
    Camera Settings
Non-linear Intensity Deformation by Automatic Camera Settings (Alismail 2017)
Visual Place Recognition – Challenges

## Slide 10: Place Recognition – Summary
Local Image Features
  Prone to appearance variations
Global Representations
  Prone to viewpoint variations
Deep-learnt features
  Robust to both
Missing
  3-D Geometric Pose for Condition-Invariant Descriptors

## Slide 11: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 12: Visual Odometry
Matching consecutive images for Ego-motion estimation
Methods
  Feature Correspondence
  Direct Whole Image Matching
  Hybrid Methods
  Deep Learning Based
Challenges
  Abrupt Appearance variations
  Low light environment
  Rapid Camera Motion
    Motion Blur
    Large Viewpoint Variation
VO Failure is catastrophic for Visual SLAM
(Alismail 2016)
CVB Optical Flow
https://www.commonvisionblox.com/en/products/series/cvb-optical-flow/

## Slide 13: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map

## Slide 14: Representation Map
Different Types of Maps
  Topological
  Metric
  Hybrid or Topometric
  Semantic
Topological Map
Time-Neighbouring Relations (Angeli 2008)
Metric Map Using LSD-SLAM
(Engel 2014)
Metric-Topological Map (Blanco 2008)
SemanticFusion: Dense 3D Semantic Mapping (McCormac 2016)

## Slide 15: Visual SLAM
Optimization
Visual Place Recognition
Visual Odometry
Representation Map
Semantics?

## Slide 16: Semantics in Vision
Type of environment
outdoor
Semantic categories:
coast:0.35, ocean:0.30, boardwalk:0.07
SUN scene attributes:
far-awayhorizon, openarea, naturallight, natural, directsunsunny, swimming
Semantics within an Image
  Object Recognition
  Sparse or Dense Object Segmentation
Place Semantics
  Place-centric
  Place Categories and Attributes
Object Detection Using Faster R-CNN (Ren 2015)
(Zhou 2014)
http://places.csail.mit.edu/demo.html

## Slide 17: Semantics in Visual SLAM
Objects as Landmarks
Semantic Mapping
Place Recognition
Multi-Object SLAM (Dharmasiri 2016)
Object-Oriented Semantic Mapping
(Sunderhauf 2017)
Object Proposals Refinement Using Roadway Semantics
(Hou 2017)

## Slide 18: Research Gap
Visual Place Recognition
  Viewpoint- and Condition-Invariant Description
  With 3D Relative Pose Estimation
Visual Odometry
  Robustness to Dynamic Conditions
  Hybrid Approach
Semantics for places
  Use Semantics to improve place recognition

## Slide 19: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 20: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 21: Characterizing System’s Response
Variations in Viewpoint and Environmental Conditions
  Visual SLAM
    Place Recognition
    Visual Odometry
  Performance Evaluation
    Using Real and Simulated Data
viewpoint- and condition-invariant
Viewpoint Varies
Time of Day

## Slide 22: Adapting to Challenging Conditions
Low Light and Rapid Camera Movement
  Hybrid Visual Odometry
    Supplement state-of-the-art system and
    Develop methods to
      Adapt System Parameters
        Eg. Image Scale Pyramid
  Address Variable Speed Across Multiple Traverses
    Improving Place Recognition Using Motion Cues
viewpoint- and condition-invariant

## Slide 23: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 24: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 25: Semantic Segmentation of Environment
Planned Approach
  Semantic Place Categorization
    Places-CNN
  Temporal Clustering of Semantic Labels
    Segment Environment
      Vehicle on Roads - Urban Canyon, Highway, Tunnel etc.
      House – Bedroom, Kitchen, Lawn, Stairs etc.
Place Categorization and Semantic Mapping (Sunderhauf 2016)
semantics-aware, condition-invariant

## Slide 26: Semantic Segmentation of Environment
  Study Appearance Variations Across Place Categories
    Effects on Place Recognition
  Develop Methods for Seamless Transitions Within Environment
    Indoor/Outdoor, Bland/Cluttered etc.
    Benchmark place recognition performance against state-of-the-art methods
semantics-aware, condition-invariant

## Slide 27: Semantic Segmentation Within Image
Planned Approach
  Use state-of-the-art semantic segmentation
    Object-level or Pixel-level
  Learn semantically salient objects/regions for place recognition
Semantic Annotations (Mottaghi 2014)
semantics-aware, condition-invariant

## Slide 28: Semantic Segmentation Within Image
  Determine Condition-Dependent Objects/Regions
  Determine Dynamic Objects
  Evaluate Performance with Semantic Masking
  Performance Benchmark for place recognition with
    A large number of dynamic objects and
    Extreme condition variations
semantics-aware, condition-invariant

## Slide 29: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 30: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 31: Appearance-Robust 3-D Relative Pose
Planned Approach
  Condition-Invariant Image Representation
    Exploring Bit-Planes Descriptor (Alismail 2016)
  Direct Image Alignment in LK framework
    Descriptor Constancy vs Brightness Constancy
Expected Outcome
  Utility for Condition-Invariant Place Recongition
  3D Relative Pose Estimation
  6-DoF Condition-Invariant Visual SLAM system
8-Channel Bit-Plane Descriptor can be used within a multi-channel LK framework using SSD cost measure (Alismail 2016)
6-DoF, condition-invariant

## Slide 32: Problem Statement
How can we develop a general purpose
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system?

## Slide 33: An Integrated System
Planned Approach
  Semantic Mapping and System Integration
    Hybrid Visual Odometry
    Visual Place Recognition
      Semantic Information
    Appearance Robust 3-D Relative Pose
Expected Outcome
  3-D Semantically-Interactive Map of Environment
  Semantic Navigation Goals
Object Oriented Semantic Mapping (Sunderhauf 2017)
6-DoF semantics-aware viewpoint- and condition-invariant visual SLAM system

## Slide 34: Work Progress
Characterizing System’s Response to Condition and Viewpoint Variations
  Performance Evaluation using High-Fidelity Simulation
  Accepted at IROS 2016
    Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M.
Adapting to Variations in Environment
  Improving Condition-Invariant Place Recognition
  Accepted at IROS 2017
    Garg, S., Jacobson, A., Kumar, S. and Milford, M.
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 35: Work Progress
Characterizing System’s Response to Condition and Viewpoint Variations
  High-fidelity simulation for evaluating robotic vision performance
    Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M.
    Accepted at IROS 2016
Adapting to Variations in Environment
  Improving Condition-Invariant Place Recognition
  Accepted at IROS 2017
    Garg, S., Jacobson, A., Kumar, S. and Milford, M.
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 36: Characterizing Visual SLAM
Performance Evaluation Using High-Fidelity Simulation
(Skinner 2016)
SeqSLAM – Place Recognition
ORB-SLAM – Visual SLAM
Viewpoint Varies
Time of Day

## Slide 37
Performance Comparison
  Real vs Simulated
Real
Simulated
Lateral Camera Offset

## Slide 38: Work Progress
Characterizing System’s Response to Condition and Viewpoint Variations
  High-fidelity simulation for evaluating robotic vision performance
    Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M.
    Accepted at IROS 2016
Adapting to Variations in Environment
  Improving Condition- and Environment-Invariant Place Recognition with Semantic Place Categorization
    Garg, S., Jacobson, A., Kumar, S. and Milford, M.
    Accepted at IROS 2017
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 39: Adapting to Variations In Environment
Semantic Place Categorization
  Using Places-CNN
    (Zhou 2014)
Label
  0 - Outdoor
  2 - Indoor

## Slide 40
Image Matching Cost Matrix
Two Traverses of Environment
SeqSLAM (Milford 2012)

## Slide 41
Parking Lot Data
  From Basement to Open Parking
Day Traverse
Night Traverse

## Slide 42: Work Progress
Characterizing System’s Response to Condition and Viewpoint Variations
  High-fidelity simulation for evaluating robotic vision performance
    Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M.
    Accepted at IROS 2016
Adapting to Variations in Environment
  Improving Condition- and Environment-Invariant Place Recognition with Semantic Place Categorization
    Garg, S., Jacobson, A., Kumar, S. and Milford, M.
    Accepted at IROS 2017
Ego-motion Estimation in Challenging Conditions
  Hybrid Visual Odometry
  Improving Place Recognition Using Motion Cues

## Slide 43: Ego-motion for Challenging Conditions
Self-Similarity Matrix

## Slide 44
Hybrid Visual Odometry System
  Supplement state-of-the-art system
    Adapt System Parameters
    Improve Place Recognition
Ground Truth
Often Accurate, But Brittle
Less Accurate, But Robust

## Slide 45: Improving Place Recognition Using Motion Cues
Dynamic Frame Sampling
  Pick frames ‘n’ units apart
Vehicle Moving in Varying Traffic Conditions
(Pepperell 2014)
Vanilla SeqSLAM
Proposed Method

## Slide 46
6-DoF Semantics-Aware Condition- and Viewpoint-Invariant Visual SLAM
System’s Response to Viewpoint and Condition Variations
Tests on Real and Simulated Data
Appearance Variations Within Environment
Semantic Map
Salient Objects/Regions for Place Recognition
Appearance-Robust Geometric Transform
System Integration
6-DoF Semantics-Aware Visual SLAM
6-DoF Condition-Invariant Visual SLAM
Condition-Invariant Image Description
Semantic Segmentation of Images
Determine Condition-Dependent and Dynamic Objects
Semantic Segmentation of Environment
Place Categorization improves Place Recognition
High-Fidelity Performance Evaluation
Robustness to Low Light and Rapid Camera Movement
Coarse Ego-motion Estimation
Supplement state-of-the-art Visual Odometry
IROS 2018
ICRA 2018
ICRA 2019
IJRR
2019
IROS 2017
IROS 2016
Research
Tasks
Proposed
Plan
Expected
Outcome
Target
Publications
Research Summary

## Slide 47: PhD Timeline

## Slide 48: References
Engel, Jakob, Thomas Schöps, and Daniel Cremers. "LSD-SLAM: Large-scale direct monocular SLAM." European Conference on Computer Vision. Springer International Publishing, 2014.
Sünderhauf, N., Neubert, P. and Protzel, P., 2013, May. Are we there yet? Challenging SeqSLAM on a 3000 km journey across all four seasons. In Proc. of Workshop on Long-Term Autonomy, IEEE International Conference on Robotics and Automation (ICRA) (p. 2013).
Alismail, H., Kaess, M., Browning, B. and Lucey, S., 2017. Direct Visual Odometry in Low Light Using Binary Descriptors. IEEE Robotics and Automation Letters, 2(2), pp.444-451.
Milford, M.J. and Wyeth, G.F., 2012, May. SeqSLAM: Visual route-based navigation for sunny summer days and stormy winter nights. In Robotics and Automation (ICRA), 2012 IEEE International Conference on (pp. 1643-1649). IEEE.
Cummins, M. and Newman, P., 2007, April. Probabilistic appearance based navigation and loop closing. In Robotics and automation, 2007 IEEE international conference on (pp. 2042-2048). IEEE.
Alismail, H., Browning, B. and Lucey, S., 2016, October. Robust tracking in low light and sudden illumination changes. In 3D Vision (3DV), 2016 Fourth International Conference on (pp. 389-398). IEEE.
Mur-Artal, R. and Tardós, J.D., 2015, July. Probabilistic Semi-Dense Mapping from Highly Accurate Feature-Based Monocular SLAM. In Robotics: Science and Systems.
Sünderhauf, N., Dayoub, F., McMahon, S., Talbot, B., Schulz, R., Corke, P., Wyeth, G., Upcroft, B. and Milford, M., 2016, May. Place categorization and semantic mapping on a mobile robot. In Robotics and Automation (ICRA), 2016 IEEE International Conference on (pp. 5729-5736). IEEE.
Hou, Y., Zhang, H., Zhou, S. and Zou, H., 2017. Use of Roadway Scene Semantic Information and Geometry-preserving Landmark Pairs to Improve Visual Place Recognition in Changing Environments. IEEE Access.

## Slide 49: References
Ren, S., He, K., Girshick, R. and Sun, J., 2015. Faster r-cnn: Towards real-time object detection with region proposal networks. In Advances in neural information processing systems (pp. 91-99).
Zhou, B., Lapedriza, A., Xiao, J., Torralba, A. and Oliva, A., 2014. Learning deep features for scene recognition using places database. In Advances in neural information processing systems (pp. 487-495).
Laffont, P.Y., Ren, Z., Tao, X., Qian, C. and Hays, J., 2014. Transient attributes for high-level understanding and editing of outdoor scenes. ACM Transactions on Graphics (TOG), 33(4), p.149.
Dharmasiri, T., Lui, V. and Drummond, T., 2016, October. MO-SLAM: Multi object SLAM with run-time object discovery through duplicates. In Intelligent Robots and Systems (IROS), 2016 IEEE/RSJ International Conference on (pp. 1214-1221). IEEE.
Jia, Y., Shelhamer, E., Donahue, J., Karayev, S., Long, J., Girshick, R., Guadarrama, S. and Darrell, T., 2014, November. Caffe: Convolutional architecture for fast feature embedding. In Proceedings of the 22nd ACM international conference on Multimedia (pp. 675-678). ACM.
Sünderhauf, N., Pham, T.T., Latif, Y., Milford, M. and Reid, I., 2016. Meaningful Maps $-$ Object-Oriented Semantic Mapping. arXiv preprint arXiv:1609.07849.
Alismail, H., Browning, B. and Lucey, S., 2016. Bit-planes: Dense subpixel alignment of binary descriptors. arXiv preprint arXiv:1602.00307.
Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M., 2016, October. High-fidelity simulation for evaluating robotic vision performance. In Intelligent Robots and Systems (IROS), 2016 IEEE/RSJ International Conference on (pp. 2737-2744). IEEE.
Mottaghi, R., Chen, X., Liu, X., Cho, N.G., Lee, S.W., Fidler, S., Urtasun, R. and Yuille, A., 2014. The role of context for object detection and semantic segmentation in the wild. In Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition (pp. 891-898).

## Slide 50: Thank You!