## Slide 1: 6-DoF Semantics-Aware Condition- and Viewpoint-Invariant Visual SLAM
Principal Supervisor : Michael Milford
Associate Supervisor: Niko Sunderhauf
Confirmation of Candidature
Sourav Garg

## Slide 2: Contents
Introduction
Literature Review
Research Questions
Research Plan
Work Progress
PhD Timeline

## Slide 3: Introduction
Social [1]
Domestic [2,3]
Industrial [4]
https://en.wikipedia.org/wiki/Pepper_(robot)#/media/File:SoftBank_pepper.JPG
Larry D. Moore CC BY-SA 3.0 -https://en.wikipedia.org/wiki/Domestic_robot#/media/File:Roomba_original.jpg
http://www.robotshop.com/en/robomow-rs622-robot-lawn-mower.html
https://en.wikipedia.org/wiki/Robot#/media/File:Automation_of_foundry_with_robot.jpg

## Slide 4: SLAM: Is it solved?
Simultaneous Localization and Mapping
Solved (Thrun and Niera [5]):
  For Static Environments
  Using Laser Rangefinder
Unsolved:
  Vision Only
  Extreme Appearance Change
  Dynamic Objects
  Semantic Understanding
[5] Frese, U., 2010. Interview: Is slam solved?. KI-Künstliche Intelligenz, 24(3), pp.255-257.

## Slide 5: Visual SLAM
Use only Visual cues
  Monocular or Stereo Vision using Digital Cameras
Components:
  Visual Odometry
  Visual Place Recognition
  Representation Map
LSD-SLAM (Engel 2014)

## Slide 6: Visual Place Recognition
Image Representation
  Local Features – SIFT, SURF, BRIEF, ORB etc.
    Bag of Words in FAB-MAP, ORB-SLAM etc.
  Global Representation – ConvNet, Bit-Planes, HoG etc.
    Direct Matching in LSD-SLAM, SeqSLAM etc.
Challenges
  Perceptual Aliasing
    Different places appear similar
  Conditions Variations (Weather, Season, Time of day)
    Same place appears different
  Viewpoint Variations

## Slide 7: Environmental Conditions
Seasonal Variations in Nordland (Sunderhauf 2013)
SeqSLAM - Sunny Days vs Stormy Nights (Milford 2012)
Non-linear Intensity Deformation by Automatic Camera Settings (Alismail 2017)

## Slide 8: Perceptual Aliasing
Different Places with Similar Appearance (Cummins 2007)

## Slide 9: Place Recognition – Review
Local Image Features
  Robust to viewpoint changes
  Prone to appearance variations
Global Representations
  Robust to appearance variations
  Prone to viewpoint variations
Deep-learned features
  Robust in both cases
  Lack relative 3D pose estimation

## Slide 10: Visual Odometry
Matching consecutive images for Ego-motion estimation
Methods
  Local Feature Tracking
    FAST, SIFT, ORB etc. based feature correspondence
  Direct Whole Image Matching
  Hybrid Methods
    Semi-Direct Visual Odometry (SVO)
  Deep VO
    PoseNet, Deep Tracking, Sfm-Net etc.
Challenges
  Local Appearance variations
  Low light environment
  Rapid Camera Motion
  Motion Blur
VO Failure is catastrophic for Visual SLAM

## Slide 11: Some Challenges in Visual Odometry
Motion Blur
Low Light Environment
Illumination Variation
(Alismail 2016)

## Slide 12: Representation Map
Types of Maps
  Topological, Metric or Topometric
3D Reconstruction of Environment
  6-DoF Visual SLAM systems
  Sparse, Semi-Dense or Dense Reconstruction
Semantics in Maps
  Meaningful interaction with environment
Aim: Metric Map with Semantic Topology

## Slide 13
Probabilistic Semi-Dense Mapping (Mur-Artal 2015)
Place Categorization and Semantic Mapping (Sunderhauf 2016)

## Slide 14: Semantics in Visual SLAM
Semantics within an Image
  Object-Oriented
    Deep-learned Object Recognition
    Sparse or Dense Object Segmentation
  Semantic Structures like wall, ceiling, floor etc.
Place Semantics
  Place-centric vs Object-centric Approach
  Place Categories and Attributes
    Structural – Train Station, Kitchen, Bedroom etc.
    Transient – Night, Rain, Snow etc.

## Slide 15
Object Detection Using Faster R-CNN (Ren 2015)
Multi-Object SLAM (Dharmasiri 2016)
Transient Attributes for Outdoor Scene Editing (Laffront 2014)
Scene Recognition Using Places Database (Zhou 2014)

## Slide 16: Problem Statement
How can we develop a general purpose 6-DoF semantics-aware condition- and viewpoint-invariant visual SLAM system?

## Slide 17: Research Questions
How can we characterize a visual SLAM system against variations in environment and ego-motion, and make it more robust for both visual place recognition and visual odometry?
How can semantic information related to images add value to a visual SLAM system?
Can we develop a general purpose 6-DoF semantics-aware SLAM system robust to condition and viewpoint variations.

## Slide 18: Research Plan
Characterizing and Adapting Visual SLAM system
  Viewpoint- and Condition-Invariance
  Adapting to Variations Within Environment
  Ego-motion Estimation for Low Light and Rapid Movement
Semantics for Visual Place Recognition
  Robust Semantic Representation
  Semantics Across Places
  Semantics Within Places
6-DoF Semantics-Aware Visual SLAM
  Condition-Invariant 3D Relative Pose Estimation
  Semantics for SLAM
  An integrated system

## Slide 19: RQ:1 - Characterizing and Adapting Visual SLAM
Characterizing Viewpoint and Condition Invariance
  Place Recognition – SeqSLAM
  Visual Odometry – ORB-SLAM
Adapting to Variations Within Environment
  Transitions in Environment
    Indoor/Outdoor, Naturally-Lit/Artificially-Lit etc.
  Environment Segmentation
    Improve Place Recognition
Ego-motion Estimation for Low Light and Rapid Movement
  Speed Estimation for Visual Odometry
  Speed-Normalized Data Sampling for Place Recognition

## Slide 20: RQ:2.1 – Robust Semantic Representation
  Transient Attributes (Laffront 2014)
    Time of Day
      Sunrise/Sunset – 0.59
    Weather
      Sunny/Direct Sun – 0.39
      Clouds/Overcast – 0.27
    Season
      Summer – 0.34
      Winter – 0.07
  Place-Centric Semantics (Zhou 2014)
    Environment Type
      Outdoor
    Categories
      Harbor -0.44
      Dock – 0.33
      Boat Deck – 0.10
    Attributes
      Open Area
      Natural Light
      Far-Away Horizon
      Man-Made
  Object-Centric Semantics (Jia 2014)
    Vessel – 1.26
    Craft – 1.17
    Vehicle – 0.80
    Ship – 0.76

## Slide 21: RQ:2.1 – Robust Semantic Representation
Planned Approach
  Method
    Deep Convolutional Neural Network
    Multi-label (2D) Classification
  Image Databases
    ImageNet, Places2, AMOS etc.
  Ground Truth Labelling
    Cross-Labelling using state-of-the-art classifiers
    Transfer Labels using Place Recognition
Anticipated Challenges
  Class Balancing
  Data Insufficiency
Expected Outcomes
  Performance benchmark for outdoor scene categorization
  Study utility for Condition-Invariant Place Recognition

## Slide 22: RQ:2.2 - Semantics Across Places
Planned Approach
  Temporal Clustering of Semantic Labels
    Segment Environment
      Office Space - Cubicles, Canteen, Corridor, Restroom etc.
      Vehicle on Roads - Urban Canyon, Highway, Tunnel etc.
Expected Outcome
Indoor-Outdoor Seamless Localization
  Categorize and Recognize in a Reduced Search Space
    Coarse Semantic Localization
    Study Computational Gain for very large databases
  Seamless Transitions Within Environment
    Indoor/Outdoor, Naturally/Artificially Lit, Bland/Cluttered
    Benchmark place recognition performance against state-of-the-art methods

## Slide 23: RQ:2.3 - Semantics Within Places
Expected Outcome
  Determine condition-invariant semantic entities
  Determine dynamic objects in environment
  Performance Benchmark for place recognition with dynamic objects and condition variations
Planned Approach
  Use state-of-the-art semantic segmentation
    Object-level or Pixel-level
  Learn semantically salient objects/patches for place recognition
Semantic Annotations (Mottaghi 2014)

## Slide 24: RQ:3.1 – Condition-Invariant 3D Relative Pose
Planned Approach
  Condition-Invariant Place Description
    Exploring Bit-Planes Descriptor (Alismail 2016)
  Direct Image Alignment in LK framework
    Assuming Descriptor Constancy as opposed to Brightness Constancy
Expected Outcome
  3D Relative Pose Estimation for Condition-Invariant Place Recognition
  6-DoF Condition-and Viewpoint-Invariant Visual SLAM system
8-Channel Bit-Plane Descriptor can be used within a multi-channel LK framework using SSD cost measure (Alismail 2016)

## Slide 25: RQ:3.2 – SLAM for Semantics
Royal Palm - 0.71
Palm – 0.95
Tree – 0.95
Plant – 0.95
Key Palm – 0.66
Tesla Coil – 0.80
Electrical Device – 0.80
Device – 0.80
Royal Palm – 0.79
Palm – 0.79
Great Hall – 0.61
Hall – 0.61
Room – 0.72
Atrium of Building – 0.61
Courtyard – 0.61
Building – 0.66
Royal Palm - 0.61
Palm – 0.73
Tree – 0.73
Plant – 0.73
IBMWatson Developer Cloud – Bluemix Visual Recognition Demo - https://visual-recognition-demo.mybluemix.net/

## Slide 26: RQ:3.2 – SLAM for Semantics
Planned Approach
  Recognize places and improve semantic labelling
    Generate a prior probability for environment labels
    Where appearance of environment has changed
    Using cues from appearance-robust place recognition
Expected Outcome
  Establish utility of place recognition for semantics
  Benchmark Object Recognition Performance within a Visual SLAM framework

## Slide 27: RQ:3.3 – An Integrated System
  Integrate the modified and newly developed components
  6-DoF Semantics-Aware Condition- and Viewpoint-Invariant Visual SLAM system
  Semantically-Interactive 3-D Map
Object Oriented Semantic Mapping (Sunderhauf 2016)

## Slide 29: Work Progress
Performance Evaluation using High-Fidelity Simulation
  Place Recognition – SeqSLAM
  Visual Odometry – ORB-SLAM
Semantic Segmentation of Environment
  Transitions in Environment
  Improve Condition-Invariant Place Recognition
Ego-motion Estimation in Unfavourable Conditions
  Hybrid Visual Odometry
  Speed-Normalized Data Sampling for Place Recognition

## Slide 30: Characterizing Visual SLAM
Performance Evaluation Using High-Fidelity Simulation
  Viewpoint- and Condition-Invariance
    Place Recognition using SeqSLAM
    Visual Odometry using ORB-SLAM
(Skinner 2016)

## Slide 31
(Skinner 2016)

## Slide 32
SeqSLAM – Place Recognition
ORB-SLAM – Visual Odometry

## Slide 33: Adapting to Environment
Semantic Segmentation of Environment
Improving Place Recognition

## Slide 34
Semantic Labels for Segmented Environment
Extreme Variations in Appearance Within Environment
Ground Truth
Vanilla SeqSLAM
Proposed Approach

## Slide 35
Performance Changes
  More pronounced with extreme variations within environment
  Global Conditions
    If similar – Global minima generally works
    If different – Depends on Query Image
  Semantics later replaced by segmentation based on image matching score

## Slide 37: Ego-motion for Unfavourable Conditions
Speed Estimation
  Low Light and Rapid Motion
  Approximate Linear Relationship between Appearance and Geometry (Lukas and Kanade 1981)
  Image Matching Score vs Frame Separation
Campus Indoor-Outdoor Dataset
Home Indoor-Outdoor Dataset

## Slide 38
Night Traverse
Day Traverse
Kelvin Grove On-Foot Dataset featuring Low Light Environment and Rapid Motion

## Slide 39
Image Matching Using
  Patch-Normalized Images with SAD Score
  Bit-Plane Descriptor with SSD Score
Polynomial fitting - SAD score and Frame Separation
Challenges
  Depends on Environment
  Is 1-D
State-of-the-art VO failure reasons
  Less features in low-light for ORB-SLAM
  Mainly rapid motion for LSD-SLAM
Possible Uses
  Hybrid approach with state-of-the-art
  Adapting parameters with change in speed

## Slide 40
Improving Place Recognition
  Speed-Normalized Data Sampling
  Ground Truth Trajectory Comparison
Vehicle Moving in Heavy Traffic Conditions
Varying Pedestrian Motion on Footpath

## Slide 41
Vehicle Moving in Heavy Traffic Conditions
Varying Pedestrian Motion on Footpath

## Slide 42: Publications To Date
Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M., 2016, October. High-fidelity simulation for evaluating robotic vision performance. In Intelligent Robots and Systems (IROS), 2016 IEEE/RSJ International Conference on (pp. 2737-2744). IEEE.
Improving Condition- and Environment-Invariant Place Recognition with Semantic Place Categorization
  Under Review - IROS 2017

## Slide 43: Target Publications
Adapting to Variations within Environment
  IROS’17
Ego-motion Estimation for Low-Light and Rapid Camera Motion
  ICRA’18
Holistic Semantic Representation
  IROS’18
Semantics Within and Across Places
  ICRA’19
Condition-Invariant Relative 3-D Pose Estimation for Condition- and Viewpoint-Invariant Visual SLAM
  IROS’19
6-DoF Semantics-Aware Visual SLAM
  IJRR/TRO

## Slide 44: PhD Timeline

## Slide 45: References
Engel, Jakob, Thomas Schöps, and Daniel Cremers. "LSD-SLAM: Large-scale direct monocular SLAM." European Conference on Computer Vision. Springer International Publishing, 2014.
Sünderhauf, N., Neubert, P. and Protzel, P., 2013, May. Are we there yet? Challenging SeqSLAM on a 3000 km journey across all four seasons. In Proc. of Workshop on Long-Term Autonomy, IEEE International Conference on Robotics and Automation (ICRA) (p. 2013).
Alismail, H., Kaess, M., Browning, B. and Lucey, S., 2017. Direct Visual Odometry in Low Light Using Binary Descriptors. IEEE Robotics and Automation Letters, 2(2), pp.444-451.
Milford, M.J. and Wyeth, G.F., 2012, May. SeqSLAM: Visual route-based navigation for sunny summer days and stormy winter nights. In Robotics and Automation (ICRA), 2012 IEEE International Conference on (pp. 1643-1649). IEEE.
Cummins, M. and Newman, P., 2007, April. Probabilistic appearance based navigation and loop closing. In Robotics and automation, 2007 IEEE international conference on (pp. 2042-2048). IEEE.
Alismail, H., Browning, B. and Lucey, S., 2016, October. Robust tracking in low light and sudden illumination changes. In 3D Vision (3DV), 2016 Fourth International Conference on (pp. 389-398). IEEE.
Mur-Artal, R. and Tardós, J.D., 2015, July. Probabilistic Semi-Dense Mapping from Highly Accurate Feature-Based Monocular SLAM. In Robotics: Science and Systems.
Sünderhauf, N., Dayoub, F., McMahon, S., Talbot, B., Schulz, R., Corke, P., Wyeth, G., Upcroft, B. and Milford, M., 2016, May. Place categorization and semantic mapping on a mobile robot. In Robotics and Automation (ICRA), 2016 IEEE International Conference on (pp. 5729-5736). IEEE.

## Slide 46: References
Ren, S., He, K., Girshick, R. and Sun, J., 2015. Faster r-cnn: Towards real-time object detection with region proposal networks. In Advances in neural information processing systems (pp. 91-99).
Zhou, B., Lapedriza, A., Xiao, J., Torralba, A. and Oliva, A., 2014. Learning deep features for scene recognition using places database. In Advances in neural information processing systems (pp. 487-495).
Laffont, P.Y., Ren, Z., Tao, X., Qian, C. and Hays, J., 2014. Transient attributes for high-level understanding and editing of outdoor scenes. ACM Transactions on Graphics (TOG), 33(4), p.149.
Dharmasiri, T., Lui, V. and Drummond, T., 2016, October. MO-SLAM: Multi object SLAM with run-time object discovery through duplicates. In Intelligent Robots and Systems (IROS), 2016 IEEE/RSJ International Conference on (pp. 1214-1221). IEEE.
Jia, Y., Shelhamer, E., Donahue, J., Karayev, S., Long, J., Girshick, R., Guadarrama, S. and Darrell, T., 2014, November. Caffe: Convolutional architecture for fast feature embedding. In Proceedings of the 22nd ACM international conference on Multimedia (pp. 675-678). ACM.
Sünderhauf, N., Pham, T.T., Latif, Y., Milford, M. and Reid, I., 2016. Meaningful Maps $-$ Object-Oriented Semantic Mapping. arXiv preprint arXiv:1609.07849.
Alismail, H., Browning, B. and Lucey, S., 2016. Bit-planes: Dense subpixel alignment of binary descriptors. arXiv preprint arXiv:1602.00307.
Skinner, J., Garg, S., Sünderhauf, N., Corke, P., Upcroft, B. and Milford, M., 2016, October. High-fidelity simulation for evaluating robotic vision performance. In Intelligent Robots and Systems (IROS), 2016 IEEE/RSJ International Conference on (pp. 2737-2744). IEEE.
Mottaghi, R., Chen, X., Liu, X., Cho, N.G., Lee, S.W., Fidler, S., Urtasun, R. and Yuille, A., 2014. The role of context for object detection and semantic segmentation in the wild. In Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition (pp. 891-898).

## Slide 47: Thank You!

## Slide 48: Research Gap
Place Recognition
  Viewpoint- and Condition-Invariance
  With 3D Relative Pose Estimation
Visual Odometry
  Robustness to Environmental Conditions
  Hybrid Approach for Rapid Camera Motion
Representation Map
  Semantic Maps on top of Geometric Maps
Semantics in Visual SLAM
  An integrated system where both can benefit